SONET
Manik Sejwal
02111502716

---
- SONET stands for Synchronous Optical Networking
- SONET is a product of the American National Standards Institute (ANSI)

---
- Synchronous optical networking (SONET) is a standardized digital communication protocol
- It is used to transmit a large volume of data over relatively long distances using a fiber optic medium
- With SONET, multiple digital data streams are transferred at the same time over optical fiber using LEDs and laser beams

---
- SONET and Synchronous Digital Hierarchy (SDH) use lasers or highly coherent light from LEDs
- It was developed to replace the plesiochronous digital hierarchy (PDH) system.
- PDH was used for transporting large amounts of telephone calls and data traffic over the same fiber without the problems of synchronization.

---
- SONET may use a re-generator for long haul distances
- Signals are transmitted into electrical signals and then re-generated into high-power signals
- At low transmission rates data can also be transferred via an electrical interface

---
- The overhead is interwoven with the payload during the process of transmission.
- The transmission alternates between overhead and payload until the completion of the transmission process
- The basic format of a SONET/SDH signal allows it to carry many different services in its virtual container (VC), because it is bandwidth-flexible

---
- SONET refers to this basic unit as an STS-3c (Synchronous Transport Signal 3, concatenated)
- The STM-1/STS-3c frame is 2,430 octets in size.
- It oper\tes three times faster than an STS-1
- Nine octets of overhead are transmitted, followed by 261 octets of payload
- This is also repeated nine times until 2,430 octets have been transmitted, also taking 125 µs

---
References
- https://en.wikipedia.org/wiki/Synchronous_optical_networking
- https://www.techopedia.com/definition/25280/synchronous-optical-networking-sonet